## Slide 1: DHCPv6 Redundancy Considerations
Redundancy Proposals in RFC 6853

## Slide 2: DHCPv4 Failover
172.16.123.45
192.168.234.56
Geographically separated DHCP Servers
Protocol-level Redundancy
Active
----------------
Active

## Slide 3: DHCPv6 Failover
Internet
Draft
draft-ietf-dhc-dhcpv6-failover-design-04
DHCPv6 Failover Design

## Slide 4: DHCPv6 Redundancy Considerations
No Redundancy Protocol
No Standards-based Failover
Deployment Models
RFC 6853

## Slide 5: Assumptions
2001:db8:bc:1::547
2001:db8:bc:2::547
2+ Servers provide DHCPv6 to same Clients

## Slide 6: Assumptions
2001:db8:bc:1::547
2001:db8:bc:2::547
DHCPv6 Servers are RFC 3315 compliant

## Slide 7: Assumptions
2001:db8:bc:1::547
2001:db8:bc:2::547
No direct Communication
DHCPv6 Replays are RFC 3315 compliant

## Slide 8: Assumptions
2001:db8:bc:1::547
2001:db8:bc:2::547
Clients
running
stateful DHCPv6

## Slide 9: Assumptions
2001:db8:bc:1::547
2001:db8:bc:2::547
Clients
have to handle Preference Option

## Slide 10: 3 semi-redundant Deployment Models
2001:db8:bc:1::547
2001:db8:bc:2::547
Split
Pools
Identical Prefixes
Multiple
Unique
Prefixes

## Slide 11: Split Pools
2001:db8:bc:1::547
2001:db8:bc:2::547
Unique, non-overlapping Pools
Simultaneously active and operational
Proprietary Mechanisms
Prefix = 2001:db8:bc:1::/64
Pool = 2001:db8:bc:1:0000::/65 Preference = 255
Prefix = 2001:db8:bc:1::/64 Pool = 2001:db8:bc:1:8000::/65 Preference = 0

## Slide 12: Multiple Unique Prefixes
2001:db8:bc:1::547
2001:db8:bc:2::547
Unique, non-overlapping Prefixes
Multiple Prefixes within the Network
No
adjacent Pools
needed
Prefix = 2001:db8:bc:1::/64 Pool = 2001:db8:bc:1::/64 Preference = 255
Prefix = 2001:db8:bc:5::/64 Pool = 2001:db8:bc:5::/64 Preference = 0

## Slide 13: Identical Prefixes
2001:db8:bc:1::547
2001:db8:bc:2::547
Overlapping Prefixes and Pools
Same Prefix, Length & Pool Definition
Prefix = 2001:db8:bc:1::/64 Pool = 2001:db8:bc:1::/64 Preference = 255
Prefix = 2001:db8:bc:1::/64 Pool = 2001:db8:bc:1::/64 Preference = 0

## Slide 14: To sum it up.
Interim Architecture
Dynamic DNS
Address Conflicts
Failure & Restore

## Slide 15: Related Request for Comments
# | Title
3315 | Dynamic Host Configuration Protocol for IPv6 (DHCPv6)
3633 | IPv6 Prefix Options for Dynamic Host Configuration Protocol (DHCP) version 6
4701 | A DNS Resource Record (RR) for Encoding Dynamic Host Configuration Protocol (DHCP) Information (DHCID RR)
4703 | Resolution of Fully Qualified Domain Name (FQDN) Conflicts among Dynamic Host Configuration Protocol (DHCP) Clients
4704 | The Dynamic Host Configuration Protocol for IPv6 (DHCPv6) Client Fully Qualified Domain Name (FQDN) Option
5007 | DHCPv6 Leasequery
5460 | DHCPv6 Bulk Leasequery
5970 | DHCPv6 Options for Network Boot
6853 | DHCPv6 Redundancy Considerations

## Slide 16: Thank you for your time.
Andreas Taudte
Sales Engineer