## Slide 1
6inACTION – Smart Communications Solution in Emergency Situations
Janez Sterle, Universität Ljubljana, Slowenien
janez.sterle@fe.uni-lj.si
Der IPv6-Kongress, Frankfurt/Main Mai 2014

## Slide 2
GEN6 – Governments ENabled with IPv6
  Project time frame
  1.1.2012 – 1.12.2014
  19 EU partners
  7 national pilots
  2 cross-border pilots
  EC reference
  http://ec.europa.eu/information_society/apps/projects/factsheet/index.cfm?project_ref=297239
  http://www.gen6-project.eu/
Slovenian pilot – A-ERCS
  Advanced Emergency Response Communication Solution
  http://www.gen6-project.eu/A-ERCS.html
  A-ERCS System deployment name 6inACTION
  http://6inaction.net/

## Slide 3
6onCORE
DISTRIBUTED AND ROBUST OVERLAY NETWORK
6onDASHBOARD
IoT-DRIVEN INTERVENTION MANAGEMENT
6onMOBILE
TRIAGE APPLICATION
6onFIRE
ON-SITE SENSOR SYSTEM
Smart and compact mobile solution designed to provide first responders with reliable communications and IoT-driven situation surveillance and intervention management services in emergency situations
Notes: So, what is the story behind the 6inACTION?
Todays professional end commercial communication systems are build, managed and provisioned as vertical separated wall gardened siloes. State od the art professional technology is TETRA(EU) or P25(USA). TETRA system is optimized for voice communications, with optional data rate of up to 9kbps – system speed. In tetra you have special features like direct mobile-to-mobile cal, p2t, group calls etc.
On the other hand state of the arte commercial mobile solution in operations is LTE, which is ALL IP packet system capable of transfering multimedia reach communication with the speed of up to 80 or 100Mbps.
If you compare state of the art technologies in the field of profesional and commercial communication system there is at least gap of 2, 3 or even 4 generations. TETRA is first generation of GSM EDGE.

## Slide 4
Fire
Flood
Water rescue
Car accidents
…
Every day operations
Source: Dalymail
Source: Wikipedia
Source: Dalymail
Professional and commercial communication systems are 100% operational

## Slide 5
Earthquake in Italy (2012)
Earthquake&Tsunami in Japan (2011)
Hurrican Katrina (2005)
Extreme natural disasters
Source: CBS
Source: Kimberly K.
Professional and commercial communication systems are down!
Source: A. Kwasinski

## Slide 6
  Different requirements for different scenarios!
High-performance communications in day-to-day operations
Survivable communications in extreme conditions
  Distributed system and service intelligence
Support for on-site intervention monitoring
  Water level, avalanche tracking, forest heatmap, hazardous substance
Firs responders mobility
  Unit, user, device, sensor
Unit monitoring and location tracking
  GPS location, indoor positioning, rescue squad vital signs
Coordinated actions across different national public safety agencies
  Fire fighters, police, ambulance, military
International intervention
  On-site and cross-border cooperation

## Slide 7
  6inACTION Vision
Converged communications in emergency situations
  a distributed and robust overlay communication solution for data transport and rich multimedia service built across professional (e.g. DMR, TETRA, Satellite) and commercial networks (e.g. UMTS/HSPA, LTE)
Commercial Operator
HSPA/LTE Coverage
Professional System
DMR/TETRA Coverage
High Performance
Ruggedized Terminals
Satellite Communications
Coverage
High Availability
IPv6 convergence layer and smart network enabler

## Slide 8
  6inACTION Vision – Technology
COTS terminals and equipment
IP67, Mil, Water Proof, Crush Proof, Drop Proof, Dust Proof,

## Slide 9
Public Safety Regulation and Standardization

## Slide 10
Regulation and standardization
  BB PPDR – BB Public Protection and Disaster Relief
  ITU-T - Report ITU-R M.2033
    Radiocommunication objectives and requirements for public protection and disaster relief
  US FCC mandates LTE for public safety network (Februar 2012)
    700 MHz, D Block
      „President Barack Obama yesterday signed into law the payroll-tax-cut extension legislation, which reallocates the 700 MHz D Block spectrum to public safety and provides $7 billion in federal funding to help pay for the buildout of a nationwide LTE network for first responders.“
      http://urgentcomm.com/policy_and_law/news/obama-signs-dblock-law-20120223
    Congressional Research Service
      Substantial radio coverage is targeted, and the act instructs leveraging existing infrastructure by establishing agreements to use commercial or other communications infrastructure already in place. (e.g., federal, state, tribal,)
  EU Regulation - CEPT ECC Report 199 (May 2013)
    User requirements and spectrum needs for future European broadband PPDR systems (Wide Area Networks)
    Frequency blocks
      400MHz, 700 MHz, 2GHz?
    Defined operational environments/category for BB PPDR
      PP1: Day-to-day operations
      PP2: Large emergency and/or public events
      DR: Disaster Relief
  Standardization - 3GPP Release 12
    http://www.3gpp.org/Public-Safety

## Slide 11
EU – 3G and LTE in Public Safety environment
  ASTRID Belgium – Public safety MVNO operator
    http://www.astrid.be

## Slide 12
6inACTION
First BB PPDR System by „CEPT ECC Report 199“

## Slide 13
6onMOBILE
SYSTEM TODAY
Backhaul
DMR
Telco UMTS/HSPA
On-site
DMR radio
SERVICES TODAY
    Voice – 1. priority
    Messages – 2. priority
SYSTEM TOMORROW
Backhaul
DMR, TETRA, satellite
Telco UMTS/HSPA, LTE, WiFi
xDSL/FTTH
On-site
DMR radio, WiFi mesh, sensors
SERVICES TOMORROW
    Voice – 1. priority
    Messages – 2. priority
    Pictures – 3. priority
    File – 4. priority
    Video – 5. priority
    Sensor & M2M services
IPv6, NEMO, PMIPv6, DSMIPv6 IPSec, …

## Slide 14
6inACTION System – High level system architecture
STRATEGIC LEVEL
TACTICAL LEVEL
TACTICAL LEVEL
USER/MISSION LEVEL
IPv6, NEMO, DSMIPv6, IPSec, …

## Slide 15
6inACTION Deployment Architecture @ Telekom Slovenije

## Slide 16
Mobile node/user provisioning – private APN
  AAA and security process
    Phase 1.: LTE/UMTS AKA – mobile provider
      USIM Authentication and Key Agreement in HSS/HLR server
    Phase 2.: Extended node/user authentication and authorization – 6inACTION system
      CHAP/PAP in Radius server
    Phase 3.: Additional encryption for the most critical services – 6inACTION system
      IPSec for networking devices (6onCORE)
      SSL VPN for end user devices (6onMOBILE)
      DSMIPv6 for sensor gateway (6onFIRE)
  Network parameter assignment
    RADIUS assigned and P-GW/GGSN enforced IPv4&IPv6 parameters - 6inACTION system
    LTE option
      IPv6 EPS bearer
      IPv4 EPS bearer
      IPv4/IPv6 EPS bearer
    HSPA/EDGE option
      IPv6 PDP context
      IPv4 PDP context
    SSL/TLS VPN option
      IPv4/IPv6
      IPv6
      IPv4

## Slide 17
6inACTION System – Detailed deployment architecture (mobile part)
Step 1.: EPS/UMTS AKA
Step 2.: PAP/CHAP@Radius
Step 3.: SSL VPN/IPSec (optional)

## Slide 18
6inACTION – Architecture for Cross-border Operations over 3G/4G
SLOVENIA
CROSS-BORDER
NATION
International
GRX/IPX
Tested IPv4/IPv6 Germany
Austria
Lithuania
Greece
Portugal






## Slide 19
IPv6 network intelligence
NEMO with MCoA and IPSec
  secure and transparent 6onCORE node mobility
SLAAC and DHCPv6
  host and network nodes auto configuration
Multicast with MLD, PIM-SM and scope options support
  flexible live multimedia streaming on-site and globally
IPv6 hierarchical addressing
  fast unit, user and sensor provisioning
BGP and OSPFv3
PA addressing
IPv6 PA and IPv4 PA addressing
IPv6, NEMO, PMIPv6, IPSec, …
Technical design
Cisco ISR819 M2M router

## Slide 20
Tactical Smart Devices

## Slide 21
TACTICAL&MISSION SMART DEVICES AND APPS
  COTS TERMINALS + IP67/MIL enclosure
    Dust proof, water proof, drop/crash proof
  INTEGRATING CUSTOM TACTICAL AND IT APPS
    Tracking, contextualized on-site triage, live video streaming
    Mail, file share, video, picture, cloud apps
  IPv6 PDP Context / EPS bearer support?
    Android:
    iOS:
✖✖
✖✖✖✖

## Slide 22
IoT-Driven Intervention Management

## Slide 23
LIVE UNIT
TRACKING
RT-SENSOR AND USER
EVENTS
IoT-DRIVEN INTERVENTION MANAGEMENT
  Real-time common operational picture
    Mash up of sensor and user events, live unit tracking, live video streaming and remotely captured on-site high resolution pictures
LIVE VIDEO
STREAMING

## Slide 24
IoT-DRIVEN INTERVENTION MANAGEMENT
  Contextualized real-time triage reporting
    User notes + site map + on-site captured high resolution picture + unit track

## Slide 25
Smart IoT Management – Hierarchical IPv6 Addressing (proposal!)
NATIONAL L./32
MOL (2a00:1368:ff::/40)
GBL /48 (2a00:1368:ff01::/48)
OZRCO /48 (2a00:1368:ff02::/48)
EPV /48 (2a00:1368:ff03::/48)
EPV1 /56
EPV2 /56 (2a00:1368:ff03:02::/56)
Municipals
Areas
Units
LAN1 /64 (2a00:1368:ff03:0201/64)
Sensor LAN2 /64 (2a00:1368:ff03:0202/64)
256 Areas
256
Municipalities
256 Units
256 Segments
Segments
Mobile Users (2a00:1368:ff00::/48)

## Slide 26
System piloting and testing

## Slide 29
System performance measurements: results for densely populated city area
RTT delay [ms]
DL Speed [Kbit/s]
- CDF (line) and histogram (bar) graph
- Blue line (IPv4) and green line (IPv6)

## Slide 30
Conclusion – IPv6&LTE for public safety?
Pros: “All IP” proven commercial technologies
  High mobile performance
    up to 95 Mbps and 10 ms data plane RTT (using LTE)
  3G/4G bullet proof system integrated security
    AKA authentication, AES/3G SNOW user and control plane encryption
    Extended authentication (i.e. RADIUS) for central user control and provisioning
    For the most critical services, additional IPSec, SSL VPN and HTTPS security services
  Standardized QoS support
  System virtualization: business APNs, MVNO, national roaming
  Standardized interfaces: various networking and handheld equipment vendors/providers
  Open and powerful ecosystem for service (multimedia, sensors, M2M) development
    Easy integration between custom services and existent IT services
  Easy cross-border and international on-site cooperation
    based on international roaming (GRX/IPX)
Cons: immature technologies in mission critical situations
  3GPP public safety standardization not finished, missing “TETRA like” features
  BB PPDR frequency band is in a process of EU allocation
  Missing IPv6 support on “some” mobiles/tablets
  Missing added value features on routing gear (i.e. NEMOv6 McA) ?
  Millions invested in TETRA

## Slide 31
Lead by ULFE, official GEN6 partner
Powered by partners
Go6 Institute – federating and consultancy role,
Ministry of Education, Science and Sport – integration of project in Slovenian government,
Water Institute - Pilot system requirements and pilot testing,
Municipality of Ljubljana (MOL), Department for Protection, Rescue and Civil Defense (OZRCO) – pilot system requirements and pilot testing, live emergency response environment & infrastructure,
Telekom Slovenije, d. d. – fixed and mobile network provider
Cisco System Slovenia&Global – networking equipment support.
Academic and Research Network of Slovenia (ARNES)